| 14 Инчов - 240 ПРОГРАМИ ПАМЕТ - ХИПЕРБАНД ТУНЕР - ТЕЛЕТЕКСТ НА БЪЛГАРСКИ - ИГРА ,КАЛЕНДАР - ФРОНТАЛЕН AV ВХОД - SLEEP TIMER | Шаси: P/N:35005218 090*K1439AXT01/00 REV. 01 (2003 година) Video CPU: STV2248C H22XA0321 CPU: MICRONAS SDA 5555 A068 CKP1605С1 |
| --- | --- |

Вход в сервизното меню – натиска се бутона MENU и 3 пъти бутона RECALL.

Смяна на factory 1, 2 ,3 ,4 с бутона MENU.

Изход от сервизното меню с бутона RECALL.

factory 1

| Rc 114 | Gc 130 | Bc 124 | Rd 41 | Gd 35 | Bd 43 |
| --- | --- | --- | --- | --- | --- |

factory 2

| PIF_VCO | 04 |
| --- | --- |
| PIF_VCO_f | 49 |
| Tuner_AGC | 56 |
| H_shift | 29 |
| V_size | 22 |
| V_shift | 12 |

factory 3

| Sound | none |
| --- | --- |
| Max_snd_sys | 03 |
| Max_bright | 50 |
| Max_contr | 45 |
| Max_color | 63 |
| Max_sharp | 12 |
| IF_38_45 | 38 Mhz |
| APR | 00 |
| Sub_Bright | 44 |
| Bell_Filter | 00 |
| Band_PS_Shift | 00 |
| Black_stretch | 02 |
| Calculator | No (Yes) |
| Remote control | Remctr 12 |
| Audio out | Tv (av) |
| Av num | 02 |

factory 4

| primary 1 | 01 |
| --- | --- |
| primary 2 | 15 |
| primary 3 | 02 |
| primary 4 | 07 |
| primary 5 | 00 |
| primary 6 | 06 |
| primary 7 | 03 |
| primary 8 | 18 |
| secondary 1 | 01 |
| secondary 2 | 01 |
| secondary 3 | 02 |
| secondary 4 | 07 |
| secondary 5 | 00 |
| secondary 6 | 06 |
| secondary 7 | 03 |
| secondary 8 | 18 |
| X26language 1 | 00 |
| X26language 2 | 02 |
| X26language 3 | 00 |
| X26language 4 | 00 |
| X26language 5 | 00 |
| X26language 6 | 00 |
| X26language 7 | 00 |
| X26language 8 | 08 |