SERVICE MANUAL

Color Television Receiver

Model:  KP2107ASTN

SPECIFICATION

#### SPICIFICATION

System        TV          PAL          D/K, B/G ,I

SECAM       D/K,B/G

AV          PAL          50/60

SECAM       50

NTSC        4.43/3.58MHz

Channel                   VHF-Low：       49.75MHz~160.25MHz；

VHF-High:        168.25MHz~456.25MHz；

UHF:             471.25MHz~863.25M

Scanning                   Line                625/525 Line

Horizontal Frequency  15625/15750 Hz

Vertical              50/60 Hz

IF Frequency               Video     38.9MHz

Sound    32.4/32.9/33.4 MHz

Chroma   34.47 MHz

34.4 MHz(SECAM)

34.65 MHz(SECAM)

Sensitivity                 VHF LOW   48 dBμV

VHF HIGH  48 dBμV

UHF        51 dBμV

Audio Output Power         7% THD ≥ 1.2W + 1.2W

Antenna Impedance          75Ω

Power Consumption          75W

Power Supply               AC  110-240V 50/60Hz

IMPORTANT SERVICE SAFETY INFORMATION

Operating the receiver outside of its cabinet or with its back removed involves a shock hazard. Work on these models should only be performed by those who are thoroughly familiar with precautions necessary when working on high voltage equipment.

Exercise care when servicing this chassis with power applied. Many B plus and high voltage RF terminals are exposed which, if carelessly contacted, can cause serious shock or result in damage to the chassis. Maintain interconnecting ground lead connections between chassis, escutcheon, picture tube dag and tuner when operating chassis.

These receivers have a "polarized" AC line cord.  The AC plug is designed to fit into standard AC outlets in one direction only.  The wide blade connects to the 'ground side' and the narrow blade connects to the 'hot side' of the AC line. This assures that the TV receiver is properly grounded to the house wiring. If an extension cord must be used, make sure it is of the 'polarized' type.

Since the chassis of this receiver is connected to one side of the AC supply during operation, service should not be attempted by anyone not familiar with the precautions necessary when working on these types of equipment.

When it is necessary to make measurements or tests with AC power applied to the receiver chassis, an Isolation Transformer must be used as a safety precaution and to prevent possible damage to transistors. The Isolation Transformer should be connected between the TV line cord plug and the AC power outlet.

Certain HV failures can increase X-ray radiation. Receivers should not be operated with HV levels exceeding the specified rating for their chassis type. The maximum operating HV specified for the chassis used in these receivers is 27kV±1.0kV at zero beam current with a liner voltage of 110/240V AC. Higher voltage may also increase the possibility of failure in the HV supply.

It is important to maintain specified values of all components in the horizontal and high voltage circuits and anywhere else in the receiver that could cause a rise in high voltage, or operating supply voltages. No changes should be made to the original design of the receiver.

Components shown in the shaded areas on the schematic diagram and identified by in the replacement parts list should be replaced only with exact factory recommended replacement parts. The use of unauthorized substitute parts man creates may create shock, fire, X-ray radiation, or other hazards.

To determine the presence of high voltage, use accurate high impedance HV meter connected between the second anode lead and the CRT dag grounding device. When servicing the High Voltage System remove static charges from it by connecting a 10K Ohm resistor in series with an insulated wire (such as test probe) between the picture tube dag and 2nd anode lead (Have AC line cord disconnected from AC supply).

The picture tube used in this receiver employ integral implosion protection. Replace with a tube of the same type number for continued safety. Do not lift picture tube by the neck. Handle the picture tube only when wearing shatterproof goggles and after discharging the high voltage completely.  Keep others without shatter proof goggles away.

Before returning the receiver to the user, perform the following safety checks:

1. Inspect all lead dress to make certain that leads are not pinched or that hardware is not lodged between the chassis and other metal parts in the receiver.

2. Replace all protective devices such as non-metallic control knobs, insulating fishpaper, cabinet backs, adjustment and compartment covers of shields, isolation resistor-capacitor networks, mechanical insulators etc.

3. To be sure that not shock hazard exists, a check for the presence of leakage current should be made at each exposed metal part having a return path to the chassis (antenna, cabinet metal, screw heads knobs and/or shafts, escutcheon, etc.) in the following manner.

Plug the AC line cord directly into a 110V/240V, AC receptacle. (Do not use an Isolation Transformer during these checks.) All checks must be repeated with the AC line cord plug connection reversed. (If necessary, a nonpolarized adapter plug must be used only for the purpose of completing these checks.)

If available, measure current using an accurate leakage current tester. Any reading of 0.35mA or more is excessive and indicates a potential shock hazard, which must be corrected before returning the receiver to the owner.

If a reliable leakage current tester is not available, this alternate method of measurement should be used. Using two clip leads, connect a 1500 Ohm, 10 Watt resistor paralleled by a 0.15MF capacitor in series with a known earth ground, such as a water pipe or conduit and the metal part to be checked. Use a VTVM or VOM with 1000 Ohms per Volt, or higher, sensitivity to measure this AC voltage drop across the resistor. Any reading of 0.35 Volt RMS of more is excessive and indicates potential shock hazard which must be corrected before returning the receiver to the owner.

ALIGNMENT PROCEDURES

PLEASE READ BEFORE ATTEMPTING SERVICE

1. Use an Isolation Transformer when performing any service on this chassis.

2. Never disconnect any leads while receiver is in operation.

3. Disconnect all power before attempting any repairs.

4. Do not short any position of the circuit while the power is on.

5. For safety reasons, replace components any with identical replacement parts (SEE PARTS LIST).

6. Before alignment, warm up the TV for at least 30 minutes and demagnetize the CRT with an external degaussing coil.

7. When removing a PCB or related component, after unfastening or changing a wire, be sure to put the wire back in its original position.

8. Inferior silicon grease can damage IC's and transistors. When replacing IC's and transistors, use only specified silicon grease. Remove all old silicon when applying new silicon.

9. Before removing the anode cap, discharge electricity because it contains high voltage.

Service Flow Chart

Power supply

check input voltage ―→ check voltage of C910 anode ―→ check Pin 4 of N901(17v)―→ check V901 ―→ check output voltage of T901 secondary coil ―→check voltage of N905,N906 Pin 3(5.0v) and N904 Pin3 (9.0V) ―→check voltage of N103 Pin 3,15,45(5v) and Pin25,54 (3.3v)

Audio circuit

check power supply of audio power amplify circuit(25V) ―→ check input audio signal of audio power amplify circuit ―→ check waveform of XS203 Pin1 Pin 5

Horizontal circuit

Check voltage of C960 anode 108V―→ check waveform of V401 Base ―→ check waveform of V402  Collector ―→ check output voltage of T402 coil ―→ check waveform of T402 Pin 8

Vertical circuit:

check voltage of C963 anode  +12V ,C964 anode  –12V→ check waveform of N103 Pin 34 Pin35 ―→ check waveform of N401 Pin 1 Pin7 ―→ check waveform of N401 Pin 5

UOC circuit:

check voltage of N103 Pin 7 (5v) and Pin32 (0v) ―→ check Pin6 (5v)―→ check waveform of N103  Pin31

# ADJUSTMENT MANUAL

Test Notices

1.	Please follow the pointed test steps and choose the right test equipment to conduct adjustment, otherwise good effect of the unit could not be obtained. Pointed bias voltage value should be ensured during test to get satisfied test result.

2. To adjust the chassis, before installing, you should write mother chip’s data into the memory N104 that being installed into this chassis and no any data except this test manual listed are promised to be modified without designer’s agreement.

3. Let the unit warm up at least 30 minutes and demagnetize the CRT and cabinet with degaussing coil before testing.



Test equipment

1. Oscilloscope

2. Voltmeter

3. Multimeter( Inside resistance: DC≥20kΩ/V, AC≥5kΩ/V)

4．High Voltmeter 40kV

5. Degaussing Coil

6．PHILIPS Pattern Signal Generator (PH5518)

IF adjustment

1 Disconnect IF end of RF Tuner.

2 Apply 12V stable power supply to N931(7805) and N933(7805) and N932(7809) input point.

3 Adjust RP121 to the middle position, then swap TV system to PAL D/K with remote control, connect PT5820 to IF input (R101 and C101 joint) and apply 95dB 38.9MHz PAL D/K signal.

4 Connect oscilloscope or digital voltmeter anode to Pin8 of N103, and cathode to GND, adjust IFT T101 with non-inductive rod until the measured point level reading on the voltmeter is 1.60±0.05V.(Core inside IFT)

5. Reconnect IF end of RF tuner after adjustment.

HF AGC adjustment

1 Receive signal (U channel)

2 Set input field strength to 60dBμV (PAL D/K)gray scale signal.

3Adjust RP120 until C119 anode is just 4.0V±0.1V。

　Factory menu

1. Press MENU button to display the main menu, then press RECALL button five times continuously to enter factory mode. Press 0 button, then RECALL button to exit factory mode.

2. After entering factory mode:

Press 1 button to adjust Horizontal：including H-BLANK（HBS0、HBST），H-POSITION（HPOS），H-SIZE（H-P0）、H TRAPEZIUM（H-P1）、H PINCUSION（H-P2），H S-CORRECTION（H-P3）、H E-W CORNER CORRECTION（H-P4）。

Press 2 button to adjust Vertical：including V PHASE（OFS）、HEIGHT（V-P1）、V SYMMETRY（V-P2）、V LINEARITY（V-P3），Angle、Bow adjustment are also Vertical adjustment.

Angle adjustment: no upper adjustment, just switch the lower right and left to adjust.

Bow adjustment: no upper adjustment, just switch the lower right and left to adjust.

Press 3 button：Select some functions

Press 4 button：Select some functions

Press 5 button：Enter into G2 mode.(This mode is for grid test)

Press 6 button：Check CUTOFF.

Press 7 button：Check DRIVE REF.

Press 8 button：Sub Brightness/Sub Contrast and Bell volume parameters setting.

Press 9 button：Memory data.

3．Press PROG.△/PROG.▽ to select test item, and VOL+/- button to adjust the value, then press RECALL button to confirm and store.

Geometry Distortion adjustment

Adjust Geometry Distortion under factory mode with remote control including: V PHASE, V SYMMETRY, V LINEARITY, H PHASE, H SIZE, H PINCUSHION, etc. RECALL must be pressed after every step finishing to store, and the adjustment must be done according to the following order.

Use 50Hz Circle Test Card with CENTER CROSS pattern as test signal, then use remote control to enter factory mode.

1) Press 1 button to adjust Hor Blanking Stop/Start until H Blank is just out the screen.

2）Vertical Phase adjustment: Press 2 button to adjust VERT Position value until V-center and the screen’s geometric center is in accordance.

3）V AMPLITUDE adjustment: Select Vert Amplitude item to adjust the vertical amplitude until it is at an appropriate position.

4）adjustment, select S-Correction item and adjust it to make the upper and lower picture symmetrical.

5）V-Linearity adjustment: Select Vert S-Symmtry item, adjust the value to make the vertical distance from upper edge to middle pattern is equal to the vertical distance from lower edge to middle pattern.

6）Press 1 button to adjust horizontal center: Adjust Hor Position item until pattern V-center and the screen’s geometric center is in accordance.

7）	Select AV mode and use 60Hz Circle Test Card with CENTER CROSS pattern as test signal, then use remote control to enter factory mode and select vertical distortion menu. Adjust 60Hz Geometry Distortion according to steps 1～6.

Repeat steps from 1) to7) until the right value is obtained.

Functions for this unit (Select different functions for different models)

1. Enter into factory mode, then press 3 button to select and adjust as the following:

Contents in factory menu 3

MSP USED：YES

Window Mode：Yes

Side AV Used：Yes

Avout Fixed：No

Alps used：Yes

HDEV3 used：No

Fast Tune：No

TeleText：Yes

Language：All

6.5M L AUTO：NO

SCART：YES

2. Press button 4，select and adjust according to the following order:

AUDIO-ONLY:NO

TILT ADJUSTMENT:NO

SVM ADJUSTMENT: NO

REALTIME CLOCK: NO

YCbCr: NO

SECAM-L:YES

AVC:NO

Grid/Focus adjustment

- Set condition is AV mode without signal and enter into factory menu, press 6 button then 5 button to adjust the brightest color line of R, G and B just appears on the screen. Exit the factory menu.

- Select CROSSHATCH and DOT signal, then set PICTURE to STANDARD mode.

3. Adjust FOCUS to make the picture on the CRT is the clearest.

Sub Brightness adjustment

Select black and white five circles pattern, set PICTURE to standard mode. Enter into factory menu, then press 8 button to adjust Bright Mid until 8~8.5 gray scale of 10 gray scale appears on the screen. (Recommend value is 25~35). Exit factory menu.

White balance adjustment

1 Apply “left black right white” signal for white balance adjustment.

2 Enter into factory menu with remote control, press EQU button to display CCU OFF character.

3 Insert I2C BUS controller plug that is used for automatic adjustment system into XS600 socket on the main board.

4 Run the program.

5 Press SPACE key or press switch on the controller socket, white balance adjustment will be operated automatically. There have three color temperature for you to adjust, if OK, “Click” will be heard.

6 Unplug I2C controller after adjustment finishing, then press CLOCK button on the remote control to restore CCU ON.

Standard：Color temperature 9300K （X=0.284  Y=0.299）

Cold color：Color temperature 12000K（X=0.272  Y=0.279）

Warm color：Color temperature 6500K （X=0.313  Y=0.329）

SOUND VOLUME OUTPUT PARAMETER

Press SWAP button to enter this submenu, then adjust data such as:

VOL 1 VALUE:20

VOL 10 VALUE:80

VOL 40 VALUE:100

VOL 70 VALUE:110

VOL 99 VALUE:120

TELETEXT SETTINGS

Press TEX ON and HOLD button to enter the submenu, then adjust the data such as:

Western Europe:（English、French、Swedish、Finnish、Czech、Slovak、German、Spanish、Portuguese、Italian、Hungarian）

|  | ADD | DATA |
| --- | --- | --- |
| TTX LAN0 | 1728 | 0 |
| TTX LAN1 | 1729 | 1 |
| TTX LAN2 | 1730 | 2 |
| TTX LAN3 | 1731 | 3 |
| TTX LAN4 | 1732 | 4 |
| TTX LAN5 | 1733 | 5 |
| TTX LAN6 | 1734 | 6 |
| TTX LAN7 | 1735 | 0 |
| FONT MAP | 1736 | 0 |
| TTX ESC LAN0 | 1737 | 0 |
| TTX ESC LAN1 | 1738 | 1 |
| TTX ESC LAN2 | 1739 | 2 |
| TTX ESC LAN3 | 1740 | 3 |
| TTX ESC LAN4 | 1741 | 4 |
| TTX ESC LAN5 | 1742 | 5 |
| TTX ESC LAN6 | 1743 | 6 |
| TTX ESC LAN7 | 1744 | 0 |

Memory check

- Enter into factory menu, press 8 button to confirm the following settings.

| CONTRAST MIN | 22 |
| --- | --- |
| CONTRAST MID | 70 |
| CONTRAST MAX | 85 |
| BRIGHT MIN | 0 |
| BRIGHT MID | 25 |
| BRIGHT MAX | 50 |
| COLOR MIN | 0 |
| COLOR MID | 60 |
| COLOR MAX | 80 |
| CVBS-2 | YES |
| SVHS | NO |

- Press 9 button to check every address data in E2PROM.（address=0~511 in memory can not be changed at will and the following data should be right.）

①	Same data

| address | data | address | data | address | data | address | data |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 13 | 20 | 108 | 1 | 255 | 6 | 413 | 95 |
| 15 | 0 | 109 | 56 | 256 | 1 | 414 | 0 |
| 16 | 0 | 110 | 0 | 271 | 33 | 415 | 1 |
| 17 | 0 | 115 | 50 | 352 | 3 | 416 | 0 |
|  |  |  |  | 360 | 0 |  |  |
| 18 | 0 | 116 | 0 | 362 | 241 | 417 | 80 |
| 19 | 68 | 119 | 93 | 363 | 0 | 418 | 0 |
| 20 | 7 | 120 | 0 | 366 | 225 | 419 | 95 |
| 21 | 0 | 127 | 2 | 367 | 115 | 420 | 96 |
| 22 | 0 | 128 | 0 | 370 | 0 | 421 | 0 |
| 23 | 0 | 129 | 1 | 371 | 25 | 422 | 0 |
| 24 | 255 | 130 | 0 | 372 | 0 | 423 | 31 |
| 25 | 0 | 131 | 2 | 373 | 16 | 424 | 112 |
| 32 | 1 | 132 | 0 | 374 | 63 | 425 | 1 |
| 34 | 1 | 133 | 98 | 375 | 0 | 428 | 130 |
| 35 | 0 | 134 | 130 | 376 | 0 | 429 | 1 |
| 36 | 0 | 135 | 2 | 377 | 32 |  |  |
| 38 | 0 | 144 | 46 | 378 | 0 |  |  |
| 40 | 1 | 145 | 0 | 379 | 0 |  |  |
| 42 | 1 | 146 | 36 | 380 | 0 |  |  |
| 44 | 0 | 147 | 0 | 381 | 248 |  |  |
| 45 | 0 | 148 | 62 | 382 | 0 |  |  |
| 46 | 0 | 149 | 0 | 383 | 248 |  |  |
| 72 | 119 | 150 | 36 | 384 | 0 |  |  |
| 73 | 0 | 151 | 0 | 385 | 248 |  |  |
| 76 | 100 | 160 | 56 | 386 | 0 |  |  |
| 77 | 21 | 161 | 0 | 387 | 8 |  |  |
| 84 | 40 | 164 | 191 | 388 | 0 |  |  |
| 85 | 0 | 165 | 14 | 389 | 24 |  |  |
| 86 | 230 | 166 | 100 | 390 | 81 |  |  |
| 87 | 0 | 167 | 57 | 392 | 240 |  |  |
| 88 | 12 | 174 | 70 | 393 | 0 |  |  |
| 89 | 0 | 175 | 1 | 398 | 0 |  |  |
| 90 | 3 | 176 | 150 | 399 | 70 |  |  |
| 91 | 210 | 177 | 0 | 400 | 0 |  |  |
| 92 | 8 | 178 | 200 | 401 | 53 |  |  |
| 93 | 49 | 179 | 0 | 402 | 0 |  |  |
| 94 | 1 | 181 | 0 | 403 | 8 |  |  |
| 95 | 255 | 184 | 0 | 404 | 0 |  |  |
| 96 | 0 | 185 | 0 | 405 | 12 |  |  |
| 97 | 20 | 186 | 0 | 406 | 0 |  |  |
| 98 | 0 | 200 | 12 | 407 | 254 |  |  |
| 101 | 53 | 252 | 3 | 410 | 2 |  |  |
| 102 | 1 | 253 | 4 | 411 | 14 |  |  |

②Different data（Select corresponding data according to different model）.

A：Table 1

| ADDRESS | DATA |
| --- | --- |
| 37 | 131 |
| 39 | 224 |
| 41 | 189 |
| 43 | 165 |
| 91 | 210 |
| 162 | 0 |
| 163 | 254 |
| 182 | 12 |
| 183 | 10 |
| 190 | 150 |
| 191 | 0 |
| 192 | 8 |
| 271 | 33 |
| 1754 | 55 |
| 1755 | 79 |
| 1756 | 65 |
| 1757 | 121 |

B：Table 2  CRT data(data shown as the following is the reference data, if  these data has been described in BOM, please see BOM)

| ADDRESS | DATA |
| --- | --- |
| 180 | 130 |
| 187 | 7 |
| 188 | 0 |
| 189 | 12 |

Key point voltages

Note: Cold ground is regarded as the reference point for these measured data if no any other explanation being made.

“-” presents the X Pin of the component(for example: N101-12 presents The 12th Pin of N101).

① Transformer voltage

| KEY POINT | TRANSFORMER 1100xxxx |
| --- | --- |
| Output voltage 1 group（V） （C960anode） | 110±0.5 |
| Output voltage 6 groups（V） (C965 anode)Sound voltage | 25.5±1.0 |

②FBT Voltage: Tube data（the following voltage value are the reference voltage, if the following three data has been described on BOM, please see BOM）.

|  | 15” |
| --- | --- |
|  | PURE FLAT |
| Filament Voltage (virtual value ) | 6.3V±0.25V |
| HK | 0.845mA | 27kv±0.5kv |
|  | 0.1mA | <30kv |

### BLOCK  DIAGRAM

# Text boxes

+45V

MSP3410

I²C

I²C

I²C

RF

+25V

AUDIO

## VIDIO

24C16

+45V

-12V

+12V

+B

+9V

+9V

+5V

+9V

+5V

5V稳压

9V稳压

+8V

+5V

+12V

-12V

+21V

+B

R,G,B

PIF

SIF

CVBSS

~220

SIF

IF

Horizontal

circuit

Vertical circuit

STV9302A

Speaker

POWER IC

STR6753

CRT

BOARD

CRT

TDA2615

IF IC

TDA4470

SAW

FILTER

TUNERR

UOC

VCT3831

SAW

FILTER