Podešavanje konfiguracije štampača  PR2 i PR2E

Štampa setup-a:

- otvoriti poklopac sa prednje strane štampača ( nije obavezno )

- pritisnuti taster STATION2 ( držati pritisnuto )

- uključiti štampač na prekidaču  I/0

- nakon zaustavljanja glave štampača pustiti taster STATION2

- ubaciti papir i sačekati da se završi štampa

- obavezno isključiti štampač na prekidaču  I/0

Izmena setup-a:

- otvoriti poklopac sa prednje strane štampača ( nije obavezno )

- istovremeno pritisnuti tastere STATION1  i  STATION2  ( držati pritisnuto )

- uključiti štampač na prekidaču  I/0

- nakon zaustavljanja glave štampača pustiti tastere STATION1  i  STATION2

- ubaciti papir i sačekati da krene štampa

- pročitati u kojoj ste komandnoj liniji, a u zavisnosti od akcije koja se izvodi odabrati jedan od tri tastera: (STATION1=CONFIRM – potvrdi ; STATION2=SKIP – menjaj ; LOCAL=CONTINUE - nastavi)

- obavezno isključiti štampač na prekidaču  I/0

Setup

| Setup Olivetti PR2E printera |  | Setup Olivetti PR2 printera |
| --- | --- | --- |
| CONFIGURATION MODE DRAFT SPEED: NORMAL LQ TYPE: NLQ1 PAPER WIDTH: FIRST LINE BUZZER: Y INTERFACE: SERIAL RS1 EMULATION: OLIVETI BAUD RATE: 9600 BIT/CHAR: 8 PARITY: EVEN STOP BIT: 1 DSR: N DCD: N PAP.EDGE DETEC.: N SPECIAL FORMS: N BIM BIDIRECT: N OLIVETTI MENU EMULATION: PR2E PASSBOOK: Y BINDING: VERTICAL SIDE: L CHAR SET: IBM/PC IBM CHAR SET: PC PC CHAR SET: 1250 (PC-WIN LATIN2) CHAR DEFINITION: DRAFT CPI: 17.1 COMPRESSED: 17.1 VERTICAL RESOL.: 1/216inch LF+CR: Y LINE LENGTH: 94 REPLY SYNCRON.: N STATUS REQUEST: NO WAIT |  | CONFIGURATION MODE EMULATION: OLIVETI EMULATION SELECTION: TEMPORARY DRAFT SPEED: NORMAL LQ TYPE: NLQ1 PAPER WIDTH: FIRST LINE BUZZER: Y INTERFACE: RS232 BAUD RATE: 9600 BIT/CHAR: 8 PARITY: EVEN STOP BIT: 1 DSR: N DCD: N PAP.EDGE DETEC.: N SPECIAL FORMS: N OLIVETTI MENU EMULATION: PR2 PASSBOOK: Y BINDING: VERTICAL CHAR GENERATOR: OLIVETTI OLIVETTI CHAR SET: YU CHAR DEFINITION: DRAFT CPI: 17.1 VERTICAL RESOLUTION: 1/216inch LF+CR: Y LINE LENGTH: 94 RESET WITH EJECT: Y REPLY SYNCRON.: N STATUS REQUEST: NO WAIT |